BMM485 module - power control

No	state	LED / white	LED / green / /12V/	LED yellow / / 24V /	LED blue	LED / red	"pwr off" server	12VDC / router, server	24V DC / concentr.
1	220V AC ON / at DRC60-B	start blink	off	off	off	off	no	off	off
2	after 10 sec.	blink	on	on	off	off	no	on	on
3	220V AC loss , / battery is OK	blink	on	on	off	off	no	on	on
4	220V AC loss , / battery is not OK , / DRC send "BAT.LOW"	blink	on	off	on	on / 1 sec.	yes / GND for / 1 sec.	on	off
5	after 20 sec.	blink	off	off	off	off	no	off	off
6	220V AC is On - / jump to No 1

BMM485 module - power control

No	state	LED / white	LED / green / /12V/	LED yellow / / 24V /	LED blue	LED / red	"pwr off" server	12VDC / router, server	24V DC / concentr.
1	220V AC ON / at DRC60-B	start blink	off	off	off	off	no	off	off
2	after 10 sec.	blink	on	on	off	off	no	on	on
3	220V AC loss , / battery is OK	blink	on	on	off	off	no	on	on
4	220V AC loss , / battery is not OK , / DRC send "BAT.LOW"	blink	on	off	on	on / 1 sec.	yes / GND for / 1 sec.	on	off
5	after 20 sec.	blink	off	off	off	off	no	off	off
6	220V AC is On - / jump to No 1